## Slide 1: Getting started into the project
Yang Wang
Softwarefirma

## Slide 2: Overview
How to build the system from scratch

## Slide 3: Step 1: Preparation
A new PSoC
My PSoC project
My PC program
PCB board
Adapter
Patch
Hardware
Software

## Slide 4: Step 2: Solder the PSoC
Check if the used pins can be accssed with the on-board headers (Accessible mostly when“GPIO on header”/“Arduino header” is primary function)
“PSoC 6 BLE Pioneer Kit Guide”, P12-16
Inaccessible
Accessible
DO NOTHING
Solder the PSoC according to the description to make the pin accessable
PSoC project

## Slide 5: Step 3: Assemble hardware

## Slide 6: Step 4: Flash the PSoC program
Click this button to flash the program to PSoC

## Slide 7: Step 5: Run PC program to start measurement
Configure the resistance you want measure
Format: [(INPUT_0, OUTPUT_0), (INPUT_1, OUTPUT_1), ….]

## Slide 8: Annex 1: The index of the points on adapter
3 | 2 | 1 | 0
11 | 10 | 9 | 8
7 | 6 | 5 | 4
15 | 14 | 13 | 12
INPUT
OUTPUT

## Slide 9: Annex 2: Explanation of returned data
1
0
K
16-bit Code
0x8000 (32768)
0x7FFF (32767)
0x0000 (0)
The retuned data is the relative resistance with respect to the initial resistance, e (R0 is set by the offset command).
We use 16 bits (0x0000 – 0xFFFF) to encode the relative resistance. (See left figure)
Code 0x0000 – 0x8000 indicates current R <= R0
Code 0x8000 – 0x7FFF indicates current R >= R0
K is the conversion limitation defined by user (can be changed by conversion factor setting command). It is defaultly set to 10. It means only the relative resistance between 0 and 10R0 is converted. The value out of range is mapped to 0x7FFF constantly .